How to add an (S)VGA driver to XFree86

                 Copyright (c) 1993, 1994 David E. Wexelblat
                              <dwex@XFree86.org>

                           Issue 1.3 - May 29, 1994

1.  Introduction

Adding support for a new SVGA chipset to XFree86 is a challenging project for
someone who wants to learn more about hardware-level programming.  It can be
fraught with hazards (in particular, crashing the machine is all too common).
But in the end, when the server comes up and functions, it is immensely sat-
isfying.

Adding support for an SVGA chipset does not change any of the basic function-
ing of the server.  It is still a dumb 8-bit PseudoColor server or 1-bit
StaticGray server.  Adding support for new hardware (e.g. accelerated chips)
is a major undertaking, and is not anywhere near formalized enough yet that
it can be documented.

Nonetheless, the driver-level programming here is a good introduction.  And
can well be the first step for adding support for an accelerated chipset, as
many are SVGA-supersets.  Writing an SVGA-level driver for the chipset can
provide a stable development platform for making use of new features (in
fact, this has been done for the S3, Cirrus, and WD accelerated chipsets, for
internal use as the accelerated servers are developed for XFree86 2.0).

Now let's get down to it.  In addition to this documentation, a stub driver
has been provided.  This should provide you a complete framework for your new
driver.  Don't let the size of this document persuade you that this is an
overly difficult task.  A lot of work has been put into making this document
as close to complete as possible; hence it should, in theory, be possible to
use this as a cookbook, and come out with a working driver when you reach the
end.  I do advise that you read it all the way through before starting.

2.  Getting Started

The first step in developing a new driver is to get the documentation for
your chipset.  I've included a list of vendor contact information that I have
collected so far (it's far from complete, so if you have any that isn't on
the list, please send it to me).  You need to obtain the databook for the
chipset.  Make sure that the person you speak to is aware that you intend to
do register-level programming (so they don't send you the EE-style
datasheet).  Ask for any example code, or developer's kits, etc.  I've
learned that at the SVGA level, in general, a databook that lists and
describes the registers is the most you can hope to find.

If you are not familiar with VGA register-level programming, you should get
(and read!) a copy of Richard Ferraro's bible (see references below).  The
best way to understand what is happening in the server is to study the work-
ings of the monochrome server's ``generic'' server, and compare it with the
documentation in Ferraro's book (be aware that there are a few errors in the
book).  You can find the generic-VGA-register handling functions in the file
``vgaHW.c''.

Once you understand what's happening in the generic server, you should study
one or more of the existing SVGA drivers.  Obtain the databook for a sup-
ported SVGA chipset, and study the documentation along with the code.  When
you have a good understanding of what that driver does over and above the
generic VGA, you will know what information you need to obtain from the data-
book for the new chipset.  Once you have this information, you are ready to
begin work on your new driver.

3.  Directory Tree Structure

Here is an outline of the directory tree structure for the source tree.  Only
directories/files that are relevant to writing a driver are presented.  The
structure for the Link Kit is presented below.

      xc/config/cf/

                  site.def
                        Local configuration customization

                  xf86site.def
                        XFree86 local configuration customization

      xc/programs/Xserver/hw/xfree86/
            The server source

                  common/
                        Files common to all of the server (XF86Config parser,
                        I/O device handlers, etc)

                              xf86.h
                                    Contains the `ScrnInfoRec' data structure

                              xf86_Option.h
                                    Contains option flags

                              compiler.h
                                    Contains in-line assembler macros and
                                    utility functions

                  os-support/
                        OS-support layer

                              assyntax.h
                                    Contains macro-ized assembler mnemonics

                              xf86_OSlib.h
                                    OS-support includes, defines, and proto-
                                    types

                  LinkKit/

                              site.def.LK
                                    Template for Link Kit site.def

                  vga256/
                        256-color VGA server directories

                              vga/
                                    The generic VGA handling code

                                          vga.h
                                                Contains the
                                                `vgaVideoChipRec' and `vgaH-
                                                WRec' data structures

                                          vgaHW.c
                                                Contains the generic-VGA-reg-
                                                ister handling functions
                                                vgaHWInit(), vgaHWSave() and
                                                vgaHWRestore().

                              drivers/
                                    Contains the SVGA driver subdirectories.
                                    Each contains an Imakefile, a .c file for
                                    the driver, and a .s file for the bank-
                                    switching functions.

                  vga2/
                        The monochrome vga server directories.  Most of the
                        files are linked from vga256, and the differences
                        handled by conditional compilation.

                              drivers/
                                    The SVGA driver subdirectories.  The
                                    `generic' VGA driver is also located
                                    here.

                  vga16/
                        The 16-color vga server directories.  Most of the
                        files are linked from vga256, and the differences
                        handled by conditional compilation.

                              drivers/
                                    The SVGA driver subdirectories.

                  VGADriverDoc/
                        This documentation and the stub driver.

The Link Kit is usually installed in /usr/X11R6/lib/Server.  The Link Kit
contains everything that is needed to relink the server.  It is possible to
write a new driver and build a new server without having even the server
source installed.

      Server/

                  site.def
                        Local configuration customization

                  include/
                        All of the include files listed under the `common'
                        directory above

                  drivers/
                        All of the SVGA drivers

                              vga2/
                                    The SVGA driver subdirectories.

                              vga16/
                                    The SVGA driver subdirectories.

                              vga256/
                                    The SVGA driver subdirectories.

                  VGADriverDoc/
                        The directory with this documentation and the stub
                        driver.  `vgaHW.c' is also copied here, for reference
                        (it is not built as part of the Link Kit).

4.  Setting Up The Build Information

This section describes the peripheral configuration and build steps that must
be performed to set up for your new driver.  The steps are the same whether
you are building from the source tree of from the Link Kit; only the loca-
tions of the files is different.  Here are the configuration steps that must
be followed:

  1.        Choose the name for your driver subdirectory and data structures.
      Since the current driver scheme allows (in fact, encourages) putting
      drivers for multiple related chipsets in a single driver, it is usually
      best to use the vendor name, rather than a chipset version.  The fact
      that older XFree86 drivers do not follow this convention should not
      deter you from using it now - most of that code was developed before
      the driver interface had been made flexible and extensible.

      For this documentation, we'll use chips from the SuperDuper Chips ven-
      dor.  Hence, we'll use `sdc' for the name of the driver.

  2.        Decide whether your driver will support the color server, the
      monochrome server, or both.  For this documentation, we will assume
      that both the color and monochrome servers will be supported.  If you
      intend to support only the color server, the steps for the monochrome
      server can be ignored.  If you intend to support only the monochrome
      server, the steps for the color server listed should be performed for
      the monochrome server, and the monochrome steps ignored.  Most of the
      existing drivers support only the color or both servers; the
      ``generic'' driver is the only driver (currently) that supports just
      the monochrome server.

  3.        Create your driver directories:

         o If you are working in the source tree, create the following direc-
           tories:

                   xc/programs/Xserver/hw/xfree86/vga256/drivers/sdc
                   xc/programs/Xserver/hw/xfree86/vga16/drivers/sdc
                   xc/programs/Xserver/hw/xfree86/vga2/drivers/sdc

         o If you are working in the Link Kit, create the following directo-
           ries:

                   /usr/X11R6/lib/Server/drivers/vga256/sdc
                   /usr/X11R6/lib/Server/drivers/vga16/sdc
                   /usr/X11R6/lib/Server/drivers/vga2/sdc

  4.        Set up the Imakefile parameters to cause your driver to be built:

         o If you are working in the source tree:

             1.  Edit the file xc/config/cf/xfree86.cf, and add `sdc' to the
                 list for the definitions for `XF86Vga256Drivers',
                 `XF86Vga16Drivers' and `XF86Vga2Drivers'.  You should put
                 `sdc' just before `generic' in the list (i.e. second last),
                 to ensure that none of the other driver's probe functions
                 incorrectly detect the `sdc' chipset .

             2.  Edit the file xc/config/cf/xf86site.def, and add the same
                 entries in this file (this is just a comment that shows the
                 default values).

             3.  Edit the site.def.LK file in xc/pro-
                 grams/Xserver/hw/xfree86/LinkKit/, and add the same entries
                 in this file.  This is the prototype `site.def' file that
                 will be installed in the Link Kit.

         o If you are working in the Link Kit, edit the file
           /usr/X11R6/lib/Server/site.def, and add `sdc' to the
           `XF86Vga256Drivers', `XF86Vga16Drivers' and `XF86Vga2Drivers' def-
           initions as described in (a) above.

  5.        Now copy the prototype files into your new directories:

         o If you are working in the source tree, copy the `stub' files as
           follows (directories are below xc/programs/Xserver):

                 Imakefile.stub =>
                       hw/xfree86/vga256/drivers/sdc/Imakefile

                 stub_driver.c =>
                       hw/xfree86/vga256/drivers/sdc/sdc_driver.c

                 stub_bank.s =>
                       hw/xfree86/vga256/drivers/sdc/sdc_bank.s

                 Imakefile.stub =>
                       hw/xfree86/vga16/drivers/sdc/Imakefile (then edit this
                       Imakefile and make the changes described in the com-
                       ments).

                 Imakefile.stub =>
                       hw/xfree86/vga2/drivers/sdc/Imakefile (then edit this
                       Imakefile and make the changes described in the com-
                       ments).

         o If you are working in the Link Kit, copy the `stub' files as fol-
           lows:

                 Imakefile.stub =>
                       /usr/X11R6/lib/Server/drivers/vga256/sdc/Imakefile

                 stub_driver.c =>
                       /usr/X11R6/lib/Server/drivers/vga256/sdc/sdc_driver.c

                 stub_bank.s =>
                       /usr/X11R6/lib/Server/drivers/vga256/sdc/sdc_bank.s

                 Imakefile.stub =>
                       /usr/X11R6/lib/Server/drivers/vga16/sdc/Imakefile
                       (then edit this Imakefile and make the changes
                       described in the comments).

                 Imakefile.stub =>
                       /usr/X11R6/lib/Server/drivers/vga2/sdc/Imakefile (then
                       edit this Imakefile and make the changes described in
                       the comments).

  6.        Edit each of the files you've just copied, and replace `stub'
      with `sdc' and `STUB' with `SDC' wherever they appear.

That's all the prep work needed.  Now it's time to work on the actual driver.

5.  The Bank-Switching Functions

The normal VGA memory map is 64k starting at address 0xA0000.  To access more
than 64k of memory, SuperVGA chipsets implement ``bank switching'' - the
high-order address bits are used to select the bank of memory in which opera-
tions will take place.  The size and number of these banks varies, and will
be spelled out in the chipset documentation.  A chipset will have zero, one
or two bank registers.  Likely the ONLY case of zero bank registers is a
generic VGA, and hence is not a concern.

Note that some of the newer chipsets (e.g. Trident 8900CL, Cirrus) allow for
a linear mapping of the video memory.  While using such a scheme would
improve the performance of the server, it is not currently supported.  Hence
there is no way to use such features for a new chipset.

Most SVGA chipsets have two bank registers.  This is the most desirable
structure (if any banking structure can be called ``desirable''), because
data can be moved from one area of the screen to another with a simple `mov'
instruction.  There are two forms of dual-banking - one where the two bank
operations define a read-only bank and a write-only bank, and one with two
read/write windows.  With the first form, the entire SVGA memory window is
used for both read a write operations, and the two bank registers determine
which bank is actually used (e.g. ET3000, ET4000).  With the second form, the
SVGA memory window is split into two read/write banks, with each bank pointer
being used to control one window.  In this case, one window is used for read
operations and the other for write operations (e.g. PVGA1/Western Digital,
Cirrus).

A chipset that has a single bank register uses that one bank for both read
and write access.  This is problematic, because copying information from one
part of the screen to another requires that the data be read in, stored, and
then written out.  Fortunately, the server is able to handle both one-bank
and two-bank chipsets; the determination of behavior is defined by an entry
in the driver data structure described below.

A driver requires that three assembly-language functions be written, in the
file `sdc_bank.s'.  These functions set the read bank - SDCSetRead(), the
write bank - SDCSetWrite(), and set both banks - SDCSetReadWrite().  For a
chipset with only one bank, all three will be declared as entry points to the
same function (see the ``tvga8900'' driver for an example).

The functions are fairly simple - the bank number is passed to the function
in register %al.  The function will shift, bitmask, etc - whatever is
required to put the bank number into the correct form - and then write it to
the correct I/O port.  For chipsets where the two banks are read-only HERE
and write-only, the SetReadWrite() function will have to do this twice - once
for each bank.  For chipsets with two independent read/write windows, the
SetReadWrite() function should use the same bank as the SetWrite() function.

A special note - these functions MUST be written in the macroized assembler
format defined in the header file ``assyntax.h''.  This will ensure that the
correct assembler code will be generated, regardless of OS.  This macroized
format currently supports USL, GNU, and Intel assembler formats.

That's all there is to the banking functions.  Usually the chipset reference
will give examples of this code; if not, it is not difficult to figure out,
especially using the other drivers as examples.

6.  The Driver Itself

Now it's time to get down to the real work - writing the major driver func-
tions in the files sdc_driver.c.  First, an overview of what the responsibil-
ities of the driver are:

  1.          Provide a chipset-descriptor data structure to the server.
      This data structure contains pointers to the driver functions and some
      data-structure initialization as well.

  2.          Provide a driver-local data structure to hold the contents of
      the chipset registers.  This data structure will contain a generic part
      and a driver-specific part.  It is used to save the initial chipset
      state, and is initialized by the driver to put the chipset into differ-
      ent modes.

  3.          Provide an identification function that the server will call to
      list the chipsets that the driver is capable of supporting.

  4.          Provide a probe function that will identify this chipset as
      different from all others, and return a positive response if the
      chipset this driver supports is installed, and a negative response oth-
      erwise.

  5.          Provide a function to select dot-clocks available on the board.

  6.          Provide functions to save, restore, and initialize the driver-
      local data structure.

  7.          Provide a function to set the starting address for display in
      the video memory.  This implements the virtual-screen for the server.

  8.          Perhaps provide a function for use during VT-switching.

  9.          Perhaps provide a function to check if each mode is suitable
      for the chipset being used.

Before stepping through the driver file in detail, here are some important
issues:

  1.          If your driver supports both the color and monochrome servers,
      you should take care of both cases in the same file.  Most things are
      the same - you can differentiate between the two with the MONOVGA
      #define.  If the 16 color server is supported, code specific to it can
      be enabled with the XF86VGA16 #define.  In most cases  it is sufficient
      to put the following near the top of the stub_driver.c file:

              #ifdef XF86VGA16
              #define MONOVGA
              #endif

  2.          The color server uses the SVGA's 8-bit packed-pixel mode.  The
      monochrome and vga16 servers uses the VGA's 16-color mode (4 bit-
      planes).  Only one plane is enabled for the monochrome server.

  3.          It is possible for you to define your monochrome driver so that
      no bank-switching is done.  This is not particularly desirable, as it
      yields only 64k of viewing area.

Keeping these things in mind, you need to find the registers from your SVGA
chipset that control the desired features.  In particular, registers that
control:

  1.          Clock select bits.  The two low-order bits are part of the
      standard Miscellaneous Output Register; most SVGA chipsets will include
      1 or 2 more bits, allowing the use of 8 or 16 discrete clocks.

  2.          Bank selection.  The SVGA chipset will have one or two regis-
      ters that control read/write bank selection.

  3.          CRTC extensions.  The standard VGA registers don't have enough
      bits to address large displays.  So the SVGA chipsets have extension
      bits.

  4.          Interlaced mode.  Standard VGA does not support interlaced dis-
      plays.  So the SVGA chipset will have a bit somewhere to control inter-
      laced mode.  Some chipsets require additional registers to be set up to
      control interlaced mode

  5.          Starting address.  The standard VGA only has 16 bits in which
      to specify the starting address for the display.  This restricts the
      screen size usable by the virtual screen feature.  The SVGA chipset
      will usually provide one or more extension bits.

  6.          Lock registers.  Many SVGA chipset prevent modification of
      extended registers unless the registers are first ``unlocked''.  You
      will need to disable protection of any registers you will need for
      other purposes.

  7.          Any other facilities.  Some chipset may, for example, require
      that certain bits be set before you can access extended VGA memory
      (beyond the IBM-standard 256k).  Or other facilities; read through all
      of the extended register descriptions and see if anything important
      leaps out at you.

If you are fortunate, the chipset vendor will include in the databook some
tables of register settings for various BIOS modes.  You can learn a lot
about what manipulations you must do by looking at the various BIOS modes.

6.1  Multiple Chipsets And Options

It is possible, and in fact desirable, to have a single driver support multi-
ple chipsets from the same vendor.  If there are multiple supported chipsets,
then you would have a series of #define's for them, and a variable `SDC-
chipset', which would be used throughout the driver when distinctions must be
made.  See the Trident and PVGA1/WD drivers for examples (the Tseng ET3000
and ET4000 are counter-examples - these were implemented before the driver
interface allowed for multiple chipsets, so this example should NOT be fol-
lowed).  Note that you should only distinguish versions when your driver
needs to do things differently for them.  For example, suppose the SDC driver
supports the SDC-1a, SDC-1b, and SDC-2 chipsets.  The -1a and -1b are essen-
tially the same, but different from the -2 chipset.  Your driver should sup-
port the -1 and -2 chipsets, and not distinguish between the -1a and -1b.
This will simplify things for the end user.

In cases where you want to give the user control of driver behavior, or there
are things that cannot be determined without user intervention, you should
use ``option'' flags.  Say that board vendors that use the SDC chipsets have
the option of providing 8 or 16 clocks.  There's no way you can determine
this from the chipset probe, so you provide an option flag to let the user
select the behavior from the XF86Config file.  The option flags are defined
in the file ``xf86_option.h''.  You should look to see if there is already a
flag that can be reused.  If so, use it in your driver.  If not, add a new
#define, and define the string->symbol mapping in the table in that file.  To
see how option flags are used, look at the ET4000, PVGA1/WD, and Trident
drivers.

6.2  Data Structures

Once you have an understanding of what is needed from the above description,
it is time to fill in the driver data structures.  First we will deal with
the `vgaSDCRec' structure.  This data structure is the driver-local structure
that holds the SVGA state information.  The first entry in this data struc-
ture is ALWAYS `vgaHWRec std'.  This piece holds the generic VGA portion of
the information.  After that, you will have one `unsigned char' field for
each register that will be manipulated by your driver.  That's all there is
to this data structure.

Next you must initialize the `SDC' structure (type `vgaVideoChipRec').  This
is the global structure that identifies your driver to the server.  Its name
MUST be `SDC', in all caps - i.e. it must match the directory name for your
driver.  This is required so that the Link Kit reconfiguration can identify
all of the requisite directories and global data structures.

The first section of this structure simply holds pointers to the driver func-
tions.

Next, you must initialize the information about how your chipset does bank
switching.  The following fields must be filled in:

  1.          ChipMapSize - the amount of memory that must be mapped into the
      server's address space.  This is almost always 64k (from 0xA0000 to
      0xAFFFF).  Some chipsets use a 128k map (from 0xA0000 to 0xBFFFF).  If
      your chipset gives an option, use the 64k window, as a 128k window
      rules out using a Hercules or Monochrome Display Adapter card with the
      SVGA.

  2.          ChipSegmentSize - the size of each bank within the ChipMapSize
      window.  This is usually also 64k, however, some chipsets split the
      mapped window into a read portion and a write portion (for example the
      PVGA1/Western Digital chipsets).

  3.          ChipSegmentShift - the number of bits by which an address will
      be shifted right to mask of the bank number.  This is log-base-2 of
      ChipSegmentSize.

  4.          ChipSegmentMask - a bitmask used to mask off the address within
      a given bank.  This is (ChipSegmentSize-1).

  5.          ChipReadBottom,ChipReadTop - the addresses within the mapped
      window in which read operations can be done.  Usually 0, and 64k,
      respectively, except for those chipset that have separate read and
      write windows.

  6.          ChipWriteBottom,ChipWriteTop - same as above, for write opera-
      tions.

  7.          ChipUse2Banks - a boolean value for whether this chipset has
      one or two bank registers.  This is used to set up the screen-to-screen
      operations properly.

There are three more fields that must be filled in:

  1.          ChipInterlaceType - this is either VGA_NO_DIVIDE_VERT or
      VGA_DIVIDE_VERT.  Some chipsets require that the vertical timing num-
      bers be divided in half for interlaced modes.  Setting this flag will
      take care of that.

  2.          ChipOptionFlags - this should always be `{0,}' in the data
      structure initialization.  This is a bitfield that contains the Option
      flags that are valid for this driver.  The appropriate bits are ini-
      tialized at the end of the Probe function.

  3.          ChipRounding - this gets set to the multiple by which the vir-
      tual width of the display must be rounded for the 256-color server.
      This value is usually 8, but may be 4 or 16 for some chipsets.

6.3  The Ident() function

The Ident() function is a very simple function.  The server will call this
function repeatedly, until a NULL is returned, when printing out the list of
configured drivers.  The Ident() function should return a chipset name for a
supported chipset.  The function is passed a number which increments from 0
on each iteration.

6.4  The ClockSelect() function

The ClockSelect() function is used during clock probing (i.e. when no
`Clocks' line is specified in the XF86Config file) to select the dot-clock
indicated by the number passed in the parameter.  The function should set the
chipset's clock-select bits according to the passed-in number.  Two dummy
values will be passed in as well (CLK_REG_SAVE, CLK_SAVE_RESTORE).  When
CLK_REG_SAVE is passed, the function should save away copies of any registers
that will be modified during clock selection.  When CLK_REG_RESTORE is
passed, the function should restore these registers.  This ensure that the
clock-probing cannot corrupt registers.

This function should return FALSE if the passed-in index value is invalid or
if the clock can't be set for some reason.

6.5  The Probe() function

The Probe() function is perhaps the most important, and perhaps the least
intuitive function in the driver.  The Probe function is required to identify
the chipset independent of all other chipsets.  If the user has specified a
`Chipset' line in the XF86Config file, this is a simple string comparison
check.  Otherwise, you must use some other technique to figure out what
chipset is installed.  If you are lucky, the chipset will have an identifica-
tion mechanism (ident/version registers, etc), and this will be documented in
the databook.  Otherwise, you will have to determine some scheme, using the
reference materials listed below.

The identification is often done by looking for particular patterns in regis-
ter, or for the existence of certain extended registers.  Or with some
boards/chipsets, the requisite information can be obtained by reading the
BIOS for certain signature strings.  The best advise is to study the existing
probe functions, and use the reference documentation.  You must be certain
that your probe is non-destructive - if you modify a register, it must be
saved before, and restored after.

Once the chipset is successfully identified, the Probe() function must do
some other initializations:

  1.          If the user has not specified the `VideoRam' parameter in the
      XF86Config file, the amount of installed memory must be determined.

  2.          If the user has not specified the `Clocks' parameter in the
      XF86Config file, the values for the available dot-clocks must be deter-
      mined.  This is done by calling the vgaGetClocks() function, and pass-
      ing it the number of clocks available and a pointer to the ClockSe-
      lect() function.

  3.          It is recommended that the `maxClock' field of the server's
      `vga256InfoRec' structure be filled in with the maximum dot-clock rate
      allowed for this chipset (specified in KHz).  If this is not filled in
      a probe time, a default (currently 90MHz) will be used.

  4.          The `chipset' field of the server's `vga256InfoRec' structure
      must be initialized to the name of the installed chipset.

  5.          If the driver will be used with the monochrome server, the
      `bankedMono' field of the server's `vga256InfoRec' structure must be
      set to indicate whether the monochrome driver supports banking.

  6.          If any option flags are used by this driver, the `ChipOption-
      Flags' structure in the `vgaVideoChipRec' must be initialized with the
      allowed option flags using the OFLG_SET() macro.

6.6  The EnterLeave() function

The EnterLeave() function is called whenever the virtual console on which the
server runs is entered or left (for OSs without virtual consoles, the func-
tion is called when the server starts and again when it exits).  The purpose
of this function is to enable and disable I/O permissions (for OSs where such
is required), and to unlock and relock access to ``protected'' registers that
the driver must manipulate.  It is a fairly trivial function, and can be
implemented by following the comments in the stub driver.

6.7  The Restore() function

The Restore() function is used for restoring a saved video state.  Note that
`restore' is a bit of a misnomer - this function is used to both restore a
saved state and to install a new one created by the server.  The Restore()
function must complete the following actions:

  1.          Ensure that Bank 0 is selected, and that any other state infor-
      mation required prior to writing out a new state has been set up.

  2.          Call vgaHWRestore() to restore the generic VGA portion of the
      state information.  This function is in the vgaHW.c file.

  3.          Restore the chipset-specific portion of the state information.
      This may be done by simply writing out the register, or by doing a
      read/modify/write cycle if only certain bits are to be modified.  Be
      sure to note the comment in the sample driver about how to handle
      clock-select bits.

6.8  The Save() function

The Save() function is used to extract the initial video state information
when the server starts.  The Save() function must complete the following
actions:

  1.          Ensure that Bank 0 is selected.

  2.          Call vgaHWSave() to extract the generic VGA portion of the
      state information.  This function is in the vgaHW.c file.

  3.          Extract the chipset-specific portion of the state information.

6.9  The Init() function

The Init() function is the second most important function in the driver
(after the Probe() function).  It is used to initialize a data structure for
each of the defined display modes in the server.  This function is required
to initialize the entire `vgaSDCRec' data structure with the information
needed to put the SVGA chipset into the required state.  The generic VGA por-
tion of the structure is initialized with a call to vgaHWInit() (also located
in vgaHW.c).

Once the generic portion is initialized, the Init() function can override any
of the generic register initialization, if necessary.  All of the other
fields are filled in with the correct initialization.  The information about
the particular mode being initialized is passed in the `mode' parameter, a
pointer to a `DisplayModeRec' structure.  This can be dereferenced to deter-
mine the needed parameters.

If you only know how to initialize certain bits of the register, do that
here, and make sure that the Restore() function does a read/modify/write to
only manipulate those bits.  Again, refer to the existing drivers for exam-
ples of what happens in this function.

6.10  The Adjust() function

The Adjust() function is another fairly basic function.  It is called when-
ever the server needs to adjust the start of the displayed part of the video
memory, due to scrolling of the virtual screen or when changing the displayed
resolution.  All it does is set the starting address on the chipset to match
the specified coordinate.  Follow the comments in the stub driver for details
on how to implement it.

6.11  The ValidMode() function

The ValidMode() function is required.  It is used to check for any chipset-
dependent reasons why a graphics mode might not be valid.  It gets called by
higher levels of the code after the Probe() stage.  In many cases no special
checking will be required and this function will simply return TRUE always.

6.12  The SaveScreen() function

The SaveScreen() function is not needed by most chipsets.  This function
would only be required if the extended registers that your driver needs will
be modified when a synchronous reset is performed on the SVGA chipset (your
databook should tell you this).  If you do NOT need this function, simply
don't define it, and put `NoopDDA' in its place in the vgaVideoChipRec struc-
ture initialization (NoopDDA is a generic-use empty function).

If you DO need this function, it is fairly simple to do.  It will be called
twice - once before the reset, and again after.  It will be passed a parame-
ter of SS_START in the former case, and SS_FINISH in the latter.  All that
needs to be done is to save any registers that will be affected by the reset
into static variables on the SS_START call, and then restore them on the
SS_FINISH call.

6.13  The GetMode() function

The GetMode() function is not used as of XFree86 1.3; its place in the
vgaVideoChipRec should be initialized to `NoopDDA'.

At some point in the future, this function will be used to enable the server
and/or a standalone program using the server's driver libraries to do inter-
active video mode adjustments.  This function will read the SVGA registers
and fill in a DisplayModeRec structure with the current video mode.

6.14  The FbInit() function

The FbInit() function is required for drivers with accelerated graphics sup-
port.  It is used to replace default cfb.banked functions with accelerated
chip-specific versions.  vga256LowlevFuncs is a struct containing a list of
functions which can be replaced.  This struct defined in vga256.h.  Examples
of FbInit() functions can be found in the et4000, pvga1 and cirrus drivers.

If you do NOT need this function, simply don't define it, and put `NoopDDA'
in its place in the vgaVideoChipRec structure initialization.

7.  Building The New Server

As in the setup work, the steps for building the server depend whether you
are working in the source tree or in the Link Kit.  Here are the steps for
the initial build after installing your new driver files:

   o If you are working in the source tree, follow these steps:

     Go to xc/programs/Xserver, and enter `make Makefile', then `make Make-
     files depend all'

   o If you are working in the Link Kit, follow these steps:

       1.  Go to /usr/X11R6/lib/Server, and enter `./mkmf'

       2.  In the same directory, enter `make'

To rebuild the server after the initial build (e.g. after making changes to
your driver):

   o      If you are working in the source tree, follow these steps:

       1.       Go to the appropriate drivers/ directory (e.g., xc/pro-
           grams/Xserver/hw/xfree86/vga256/drivers), and enter `make'.

       2.       Go to xc/programs/Xserver, and enter `make loadXF86_SVGA' (to
           link the color server), `make loadXF86_VGA16' (to link the 16
           color server) or `make loadXF86_Mono' (to link the mono server).

   o      If you are working in the Link Kit, follow these steps:

       1.       Go to the appropriate driver directory, and enter `make'.

       2.       Go to /usr/X11R6/lib/server, and enter `make loadXF86_SVGA'
           (to link the color server) or `make loadXF86_VGA16' (to link the
           16 color server) or `make loadXF86_Mono' (to link the mono
           server).

8.  Debugging

Debugging a new driver can be a painful experience, unfortunately.  It is
likely that incorrect programming of the SVGA chipset can lock up your
machine.  More likely, however, is that the display will be lost, potentially
requiring a reboot to correct.  It is HIGHLY recommended that the server be
run from an attached terminal or a network login.  This is the only rational
way in which a debugger can be used on the server.  Attempting to use multi-
ple VTs for debugging is basically a waste of time.

Because of the potential for locking up the machine, it is a VERY good idea
to remember to do a `sync' or two before starting the server.  In addition,
any unnecessary filesystems should be unmounted while the debugging session
is going on (to avoid having to run unnecessary fsck's).

By default the server is built without debugging symbols.  The server can
grow VERY large with debugging enabled.  It is very simple to rebuild your
driver for debugging, though.  Do the following:

  1.  Go to the driver directory.

  2.  Edit the Makefile.  Look for the SECOND definition of `CDEBUGFLAGS'.
      Change this definition to

                     CDEBUGFLAGS = -g -DNO_INLINE

      (this will enable debugging symbols and disable inlining of functions,
      which can make single-stepping a nightmare).

  3.  Remove the `sdc_driver.o' file.

  4.  Now follow the steps above for rebuilding the server.

      (Alternatively, instead of editing the Makefile, you can simply do
      `make CDEBUGFLAGS="-g -DNO_INLINE"' after removing the old .o file,
      then rebuild the server as described above).

This will give you a server with which you can set breakpoints in the driver
functions and single-step them.  If you are working in the source tree, and
just learning about SVGA programming, it may be useful to rebuild vgaHW.c
with debugging as well.

9.  Advice

I cannot stress this enough - study all available references, and the exist-
ing code, until you understand what is happening.  Do this BEFORE you begin
writing a driver.  This will save you a massive amount of headache.  Try to
find a driver for a chipset that is similar to yours, if possible.  Use this
as an example, and perhaps derive your driver from it.

Do not let the gloom-and-doom in the debugging section  discourage you.
While you will probably have problems initially (I still do), careful, delib-
erate debugging steps can bear fruit very quickly.  It is likely that, given
a good understanding of the chipset, a driver can be written and debugged in
a day or two.  For someone just learning about this kind of programming, a
week is more reasonable.

10.  Advanced Topics

Newer chipsets are getting into two advanced areas: programmable clock gener-
ators, and accelerated capabilities (BitBlt, line drawing, HW cursor).  These
are new areas, and the formal interfaces to them are not yet defined.  It is
advised that you contact the XFree86 team and get involved with the develop-
ment/beta-testing team if you need to be working in these areas.

11.  References

   o Programmer's Guide to the EGA and VGA Cards, 3rd ed.

     Richard Ferraro

     Addison-Wesley, 1994

     ISBN 0-201-62490-7

     (This is the bible of SVGA programming - it has a few errors, so watch
     out.  The third edition also covers several accelerated video cards.)

   o vgadoc4.zip

     Finn Thoegersen

     (This is a collection of SVGA and other chipset documentation.  It is
     available on most MS-DOS/Windows related FTP archives, including
     wuarchive.  It is DOS/BIOS oriented, but is still extremely useful,
     especially for developing probe functions.)

12.  Vendor Contact Information

      ATI Technologies (VGA-Wonder, Mach8, Mach32, Mach64)
                 33 Commerce Valley Drive East" Thornhill, Ontario

            Canada L3T 7N6

            (905) 882-2600 (sales)

            (905) 882-2626 (tech support)

            (905) 764-9404 (BBS)

            (905) 882-0546 (fax)

      Chips & Technologies
            ???

      Cirrus Logic (SVGA, Accelerators - CL-GD5426)
            3100 West Warren Ave.

            Fremont, CA  94538

            (510) 623-8300 (N. CA, USA)

            (49) 8152-40084 (Germany)

            (44) 0727-872424 (UK)

      Genoa Systems (GVGA)
            75 E. Trimble Road

            San Jose, CA 95131

            (408) 432-9090 (sales)

            (408) 432-8324 (tech support)

      Headland Technologies, Inc (Video-7 VGA 1024i, VRAM II)
            46221 Landing Parkway

            Fremont, CA  94538

            (415) 623-7857

      Oak Technology, Inc (OTI-067,OTI-077)
            139 Kifer Ct.

            Sunnyvale, CA 94086

            (408) 737-0888

            (408) 737-3838 (fax)

      S3 (911, 924, 801/805, 928, 864, 868, 964, 968, 764, 765)
            (408) 980-5400

      Trident Microsystems Inc (8800, 8900, 9000)
            205 Ravendale Dr

            Mountainside, CA 94043

            (415) 691-9211

      Tseng Labs Inc,
            6 Terry Drive

            Newtown, PA  18940

            (215) 968-0502

      Weitek (Power9000, 5186)
            1060 E. Arques Ave,

            Sunnyvale, CA  94086

            (408) 738-5765

      Western Digital
            (714) 932-4900

     Generated from XFree86: xc/programs/Xserver/hw/xfree86/doc/sgml/VGADriv.sgml,v 3.13.2.1 1998/02/01 16:04:54 robin Exp $

     $XConsortium: VGADriv.sgml /main/9 1996/10/28 05:13:22 kaleb $